## Slide 1: Korea’s EE Key developments in 2012 < 40th APEC EGEE&C Meeting >
November 8-9, 2012
Jennifer KIM
jennifer@kemco.or.kr
KEMCO

## Slide 2
KEMCO
Contents
Overview of Korea’s Energy Efficiency programs
EE Management of Electric Heating Equipment
Designation of Energy Intensive Equipment
as EE Management target products
Establishing Plans for Standby Korea 2015

## Slide 3
KEMCO
Overview of Korea’s EE Program
3 programs in Energy Labels & Standards
High-efficiency Equipment Certification Program
e-Standby Program
Energy Efficiency Label and Standard Program
(including MEPS)
Voluntary
39 items : LED Lighting
equipment, etc
Mandatory & Voluntary
Standby Korea 2015
22 items : Computers, etc
Mandatory
5-grade labeling & MEPS
37 items : Refrigerators, Air-conditioners,
TVs, Window sets, etc

## Slide 4
KEMCO
EE Mgmt of Electric Heating Equipment

## Slide 5
KEMCO
EE Mgmt of Electric Heating Equipment
Implementing electric rates displaying scheme
Electric fan heaters
Electric stoves

## Slide 6
KEMCO
EE Mgmt of Electric Heating Equipment
Monthly energy cost
(applied big progressive rate, 384 KWR/kWh)
Please aware that you will have big energy charges if you use this product for a long time
Power consumption (W)
Name of model
CO2 emission per hour (g/h)
Label for electric fan heaters

## Slide 7
KEMCO
EE Mgmt of Electric Heating Equipment
Switching to EE L&S Program for VRF multi-split
heat pumps
Test Condition
- Model scope : Unit model of outdoor
- Pipeline length : 50m
- Heating temperature : 7℃, -15℃
Unit
Model
R | Grade
3.5 ≤ R | 1
3.25 ≤ R < 3.50 | 2
3.00 ≤ R < 3.25 | 3
2.75 ≤ R < 3.00 | 4
2.40 ≤ R < 2.75 | 5
R = EERa = (IEER+COP)/2 | 
MEPS & Energy Efficiency Level
(unit : W/W) |  |  | 
EERa | IEER (100%, 75%, 50%, 25%) | COP | COP2 (-15℃)
2.40 | 2.80 | 2.00 | 1.50
EERa = (IEER+COP)/2 |  |  | 

## Slide 8
KEMCO
Designation of Energy Intensive Equipment
as EE Mgmt Target Products
New Target Products
in Energy Efficiency Label & Standards Program
Electric fan heaters, Electric stoves (Dec. 15th. 2011)
VRF multi-split heat pumps (April. 1st. 2012)
TVs, Window sets, Transformers, Dehumidifiers
(July. 1st. 2012)
Tyres (Dec. 1st. 2012)

## Slide 9
KEMCO
Adopting MEPS & E E grade(1 to 5) for TVs
  KS C IEC 62087
R(Energy Efficiency Level Index)
  =
Power consumption at operational mode (W)
The square root of display area (sqrt(m2))
R | Standby power (passive standby mode) | Level
R ≤ 130 | ≤ 1.0W | 1
R ≤ 165 | - | 2
165 < R ≤ 205 | - | 3
205 < R ≤ 260 | - | 4
260 < R ≤ 440 | - | 5
Designation of Energy Intensive Equipment
as EE Mgmt Target Products

## Slide 10
KEMCO
Standby Korea
2015
Standby Power 0.5W
by 2015
Networked standby
: Mandatory of Set-top boxes’ Passive standby power mode
Adopting TEC
(Typical Energy Consumption)
: Computers, etc
Adopting On-mode
: Monitors
Establishing Plans for Standby Korea 2015

## Slide 11
KEMCO
Adopting TEC standard for Computers
  Energy Star Program Ver. 5.0
  ECMA-383 Categories and Allowances for Desktop and Notebook Discrete Graphics
Platform | Requirements | Capability Adjustments
Notebooks | TEC (kWh) Cat A: 40.0 Cat B: 53.0 Cat C: 88.5 | Memory: 0.4 kWh (per GB over 4 GB) Discrete GPU (FB Width): ECMA-383 Categories Additional storage: 3 kWh Discrete TV tuner : 2.1kWh
Desktop, Integrated DT | TEC (kWh) Cat A: 148 Cat B: 175 Cat C: 209 Cat D: 234 | Memory: 1 kWh (per GB over base) Base Memory: CAT A, B, and C 2GB; CAT D 4GB Discrete GPU (FB Width): ECMA-383 Categories Additional storage: 25 kWh Discrete TV tuner : 14kWh Discrete Audio card : 14kWh
Establishing Plans for Standby Korea 2015

## Slide 12
KEMCO
TEC power consumption (kWh)
  = (8760/1000) x (Poff x Toff + Psleep x Tsleep
  + Pidle x Tidle)
TEC Weighting |  | 
 | Desktop, Integrated DT | Notebook
Toff | 55% | 60%
Tsleep | 5% | 10%
Tidle | 40% | 30%
Establishing Plans for Standby Korea 2015

## Slide 13
KEMCO
Adopting On-mode standard for Monitors
  Energy Star Program Ver. 5.0
Requirements |  |  | 
Category | On-mode Power Consumption | Sleep mode | Off mode
Screen size < 76cm Megapixels ≤ 1.1MP | 6 x megapixels+ 0.00775 x viewable area + 3 | ≤2.0W | ≤0.5W
Screen size < 76cm Megapixels > 1.1MP | 9 x megapixels+ 0.00775 x viewable area + 3 |  | 
Screen size 76-153cm | 0.04185 x viewable area + 8 |  | 
Establishing Plans for Standby Korea 2015

## Slide 14
KEMCO
For more information,
E- mail : jennifer@kemco.or.kr
KEMCO homepage : http://www.kemco.or.kr/eng
Thank you!!
감사합니다.